TRL LIMITED

(C) COPYRIGHT 2006

CAPACITIES, QUEUES, AND DELAYS AT 3 OR 4-ARM MAJOR/MINOR PRIORITY JUNCTIONS

PICADY 5.1  ANALYSIS PROGRAM

RELEASE 4.0 (SEPT 2008)

ADAPTED FROM PICADY/3 WHICH IS CROWN COPYRIGHT

BY PERMISSION OF THE CONTROLLER OF HMSO

--------------------------------------------------------

FOR SALES AND DISTRIBUTION INFORMATION,

PROGRAM ADVICE AND MAINTENANCE CONTACT:

TRL SOFTWARE BUREAU

TEL: CROWTHORNE (01344) 770758, FAX: 770356

EMAIL: Software@trl.co.uk

--------------------------------------------------------

Run with file:-

"C:\Documents and Settings\Aiofe\Local Settings\temp\PICADY 5\PICADY5.vpi"

(drive-on-the-left) at 13:36:20 on Monday, 22 November 2010

.RUN INFORMATION

***************

RUN TITLE       : O'Denaney Gardens

LOCATION        : Infirmary Road/ Montpelllier Road

DATE            : 22/11/10

CLIENT          : Dublin City Council

ENUMERATOR      :

JOB NUMBER      : 110/A59

STATUS          : TIA

DESCRIPTION     :

.MAJOR/MINOR JUNCTION CAPACITY AND DELAY

***************************************

INPUT DATA

----------

MAJOR ROAD (ARM C) --------------------- MAJOR ROAD (ARM A)

I

I

I

I

I

I

MINOR ROAD (ARM B)

ARM A IS Infirmary Road North

ARM B IS Montpellier Road

ARM C IS Infirmary Road South

.STREAM LABELLING CONVENTION

---------------------------

STREAM  A-B  CONTAINS TRAFFIC GOING FROM ARM  A TO ARM B

STREAM  B-AC CONTAINS TRAFFIC GOING FROM ARM  B TO ARM A AND TO ARM  C

ETC.

.GEOMETRIC DATA

--------------

--------------------------------------------------------------------------------------

I                DATA ITEM                                       I   MINOR ROAD B    I

--------------------------------------------------------------------------------------

I  TOTAL MAJOR ROAD CARRIAGEWAY WIDTH                            I ( W  )  8.00 M.   I

I  CENTRAL RESERVE WIDTH                                         I (WCR )  0.00 M.   I

I                                                                I                   I

I  MAJOR ROAD RIGHT  TURN - WIDTH                                I (WC-B)  0.00 M.   I

I                         - VISIBILITY                           I (VC-B)120.00 M.   I

I                         - BLOCKS TRAFFIC                       I          YES      I

I                                                                I                   I

I  MINOR ROAD - VISIBILITY TO LEFT                               I (VB-C) 120.0 M.   I

I             - VISIBILITY TO RIGHT                              I (VB-A) 120.0 M.   I

I             - LANE 1 WIDTH                                     I (WB-C)  4.00 M.   I

I             - LANE 2 WIDTH                                     I (WB-A)  0.00 M.   I

--------------------------------------------------------------------------------------

.SLOPES AND INTERCEPT

--------------------

(NB:Streams may be combined, in which case capacity will be adjusted)

---------------------------------------------------------

I Intercept For Slope For Opposing   Slope For Opposing I

I STREAM B-C     STREAM  A-C          STREAM A-B        I

---------------------------------------------------------

I     769.51            0.27                0.11        I

---------------------------------------------------------

--------------------------------------------------------------------------------------------------

I Intercept For Slope For Opposing   Slope For Opposing   Slope For Opposing   Slope For OpposingI

I STREAM B-A     STREAM  A-C          STREAM A-B          STREAM  C-A          STREAM  C-B       I

--------------------------------------------------------------------------------------------------

I     635.97            0.27                0.11                  0.17                0.38       I

--------------------------------------------------------------------------------------------------

---------------------------------------------------------

I Intercept For Slope For Opposing   Slope For Opposing I

I STREAM C-B     STREAM  A-C          STREAM A-B        I

---------------------------------------------------------

I     643.46            0.23                0.23        I

---------------------------------------------------------

(NB These values do not allow for any site specific corrections)

.TRAFFIC DEMAND DATA

-------------------

-----------------------

I ARM I FLOW SCALE(%) I

-----------------------

I A   I      100      I

I B   I      100      I

I C   I      100      I

-----------------------

.Demand set:        O'Denaney Gardens

TIME PERIOD BEGINS 07.45 AND ENDS  09.15

LENGTH OF TIME PERIOD  -   90 MIN.

LENGTH OF TIME SEGMENT -   15 MIN.

.DEMAND FLOW PROFILES ARE SYNTHESISED FROM TURNING COUNT DATA

------------------------------------------------------------------------------------

I        I   NUMBER OF MINUTES FROM START WHEN    I   RATE OF FLOW (VEH/MIN)       I

I  ARM   I FLOW STARTS I TOP OF PEAK I FLOW STOPS I BEFORE I AT TOP  I AFTER       I

I        I   TO RISE   I  IS REACHED I FALLING    I  PEAK  I OF PEAK I PEAK        I

I        I             I             I            I        I         I             I

------------------------------------------------------------------------------------

I ARM  A I     15.00   I     45.00   I    75.00   I 10.32  I  15.49  I 10.32       I

I ARM  B I     15.00   I     45.00   I    75.00   I  1.41  I   2.12  I  1.41       I

I ARM  C I     15.00   I     45.00   I    75.00   I  8.14  I  12.21  I  8.14       I

------------------------------------------------------------------------------------

.Demand set:        O'Denaney Gardens

-----------------------------------------------------------

I                    I         TURNING PROPORTIONS        I

I                    I         TURNING COUNTS             I

I                    I        (PERCENTAGE OF H.V.S)       I

I                    --------------------------------------

I        TIME        I FROM/TO I ARM  A I ARM  B I ARM  C I

-----------------------------------------------------------

I   07.45 - 08.00    I         I        I        I        I

I                    I ARM  A  I  0.000 I  0.056 I  0.944 I

I                    I         I    0.0 I   46.0 I  780.0 I

I                    I         I (  0.0)I ( 10.0)I ( 10.0)I

I                    I         I        I        I        I

I                    I ARM  B  I  0.274 I  0.000 I  0.726 I

I                    I         I   31.0 I    0.0 I   82.0 I

I                    I         I ( 10.0)I (  0.0)I ( 10.0)I

I                    I         I        I        I        I

I                    I ARM  C  I  0.773 I  0.227 I  0.000 I

I                    I         I  503.0 I  148.0 I    0.0 I

I                    I         I ( 10.0)I ( 10.0)I (  0.0)I

I                    I         I        I        I        I

-----------------------------------------------------------

TURNING PROPORTIONS ARE CALCULATED FROM TURNING COUNT DATA

DEFAULT PROPORTIONS OF HEAVY VEHICLES ARE USED

.              QUEUE AND DELAY INFORMATION FOR EACH 15 MIN TIME SEGMENT

--------------------------------------------------------

FOR COMBINED DEMAND SETS

AND FOR TIME PERIOD        1

.------------------------------------------------------------------------------------------------------------------

I  TIME      DEMAND  CAPACITY  DEMAND/   PEDESTRIAN  START   END       DELAY     GEOMETRIC DELAY   AVERAGE DELAY I

I         (VEH/MIN) (VEH/MIN) CAPACITY      FLOW     QUEUE  QUEUE    (VEH.MIN/      (VEH.MIN/      PER ARRIVING  I

I                               (RFC)    (PEDS/MIN) (VEHS) (VEHS)  TIME SEGMENT)  TIME SEGMENT)    VEHICLE (MIN) I

I 07.45-08.00                                                                                                    I

I   B-AC      1.42      7.46    0.190                0.00   0.23        3.3                            0.16      I

I   C-A       6.31                                                                                               I

I   C-B       1.86      7.39    0.251                0.00   0.33        4.7                            0.18      I

I   A-B       0.58                                                                                               I

I   A-C       9.79                                                                                               I

I                                                                                                                I

.------------------------------------------------------------------------------------------------------------------

.------------------------------------------------------------------------------------------------------------------

I  TIME      DEMAND  CAPACITY  DEMAND/   PEDESTRIAN  START   END       DELAY     GEOMETRIC DELAY   AVERAGE DELAY I

I         (VEH/MIN) (VEH/MIN) CAPACITY      FLOW     QUEUE  QUEUE    (VEH.MIN/      (VEH.MIN/      PER ARRIVING  I

I                               (RFC)    (PEDS/MIN) (VEHS) (VEHS)  TIME SEGMENT)  TIME SEGMENT)    VEHICLE (MIN) I

I 08.00-08.15                                                                                                    I

I   B-AC      1.69      6.67    0.254                0.23   0.33        4.8                            0.20      I

I   C-A       7.54                                                                                               I

I   C-B       2.22      6.93    0.320                0.33   0.46        6.7                            0.21      I

I   A-B       0.69                                                                                               I

I   A-C      11.69                                                                                               I

I                                                                                                                I

.------------------------------------------------------------------------------------------------------------------

.------------------------------------------------------------------------------------------------------------------

I  TIME      DEMAND  CAPACITY  DEMAND/   PEDESTRIAN  START   END       DELAY     GEOMETRIC DELAY   AVERAGE DELAY I

I         (VEH/MIN) (VEH/MIN) CAPACITY      FLOW     QUEUE  QUEUE    (VEH.MIN/      (VEH.MIN/      PER ARRIVING  I

I                               (RFC)    (PEDS/MIN) (VEHS) (VEHS)  TIME SEGMENT)  TIME SEGMENT)    VEHICLE (MIN) I

I 08.15-08.30                                                                                                    I

I   B-AC      2.07      5.48    0.378                0.33   0.59        8.4                            0.29      I

I   C-A       9.23                                                                                               I

I   C-B       2.72      6.30    0.431                0.46   0.74       10.4                            0.28      I

I   A-B       0.84                                                                                               I

I   A-C      14.31                                                                                               I

I                                                                                                                I

.------------------------------------------------------------------------------------------------------------------

.------------------------------------------------------------------------------------------------------------------

I  TIME      DEMAND  CAPACITY  DEMAND/   PEDESTRIAN  START   END       DELAY     GEOMETRIC DELAY   AVERAGE DELAY I

I         (VEH/MIN) (VEH/MIN) CAPACITY      FLOW     QUEUE  QUEUE    (VEH.MIN/      (VEH.MIN/      PER ARRIVING  I

I                               (RFC)    (PEDS/MIN) (VEHS) (VEHS)  TIME SEGMENT)  TIME SEGMENT)    VEHICLE (MIN) I

I 08.30-08.45                                                                                                    I

I   B-AC      2.07      5.47    0.379                0.59   0.60        9.0                            0.29      I

I   C-A       9.23                                                                                               I

I   C-B       2.72      6.30    0.431                0.74   0.75       11.1                            0.28      I

I   A-B       0.84                                                                                               I

I   A-C      14.31                                                                                               I

I                                                                                                                I

.------------------------------------------------------------------------------------------------------------------

.------------------------------------------------------------------------------------------------------------------

I  TIME      DEMAND  CAPACITY  DEMAND/   PEDESTRIAN  START   END       DELAY     GEOMETRIC DELAY   AVERAGE DELAY I

I         (VEH/MIN) (VEH/MIN) CAPACITY      FLOW     QUEUE  QUEUE    (VEH.MIN/      (VEH.MIN/      PER ARRIVING  I

I                               (RFC)    (PEDS/MIN) (VEHS) (VEHS)  TIME SEGMENT)  TIME SEGMENT)    VEHICLE (MIN) I

I 08.45-09.00                                                                                                    I

I   B-AC      1.69      6.66    0.254                0.60   0.35        5.4                            0.20      I

I   C-A       7.54                                                                                               I

I   C-B       2.22      6.93    0.320                0.75   0.48        7.5                            0.21      I

I   A-B       0.69                                                                                               I

I   A-C      11.69                                                                                               I

I                                                                                                                I

.------------------------------------------------------------------------------------------------------------------

.------------------------------------------------------------------------------------------------------------------

I  TIME      DEMAND  CAPACITY  DEMAND/   PEDESTRIAN  START   END       DELAY     GEOMETRIC DELAY   AVERAGE DELAY I

I         (VEH/MIN) (VEH/MIN) CAPACITY      FLOW     QUEUE  QUEUE    (VEH.MIN/      (VEH.MIN/      PER ARRIVING  I

I                               (RFC)    (PEDS/MIN) (VEHS) (VEHS)  TIME SEGMENT)  TIME SEGMENT)    VEHICLE (MIN) I

I 09.00-09.15                                                                                                    I

I   B-AC      1.42      7.45    0.190                0.35   0.24        3.7                            0.17      I

I   C-A       6.31                                                                                               I

I   C-B       1.86      7.39    0.251                0.48   0.34        5.3                            0.18      I

I   A-B       0.58                                                                                               I

I   A-C       9.79                                                                                               I

I                                                                                                                I

.------------------------------------------------------------------------------------------------------------------

.

QUEUE FOR STREAM    B-AC

-------------------------

TIME          NO. OF

SEGMENT       VEHICLES

ENDING        IN QUEUE

08.00           0.2

08.15           0.3

08.30           0.6    *

08.45           0.6    *

09.00           0.3

09.15           0.2

.

QUEUE FOR STREAM    C-B

-------------------------

TIME          NO. OF

SEGMENT       VEHICLES

ENDING        IN QUEUE

08.00           0.3

08.15           0.5

08.30           0.7    *

08.45           0.7    *

09.00           0.5

09.15           0.3

QUEUEING DELAY INFORMATION OVER WHOLE PERIOD

--------------------------------------------

---------------------------------------------------------------------------

I STREAM I   TOTAL DEMAND  I   * QUEUEING *      I * INCLUSIVE QUEUEING * I

I        I                 I    * DELAY *        I       * DELAY *        I

I        I----------------------------------------------------------------I

I        I  (VEH)  (VEH/H) I  (MIN)    (MIN/VEH) I    (MIN)     (MIN/VEH) I

---------------------------------------------------------------------------

I  B-AC  I  155.5 I  103.7 I    34.6 I    0.22   I      34.6  I    0.22   I

I  C-A   I  692.3 I  461.6 I         I           I            I           I

I  C-B   I  203.7 I  135.8 I    45.8 I    0.22   I      45.8  I    0.22   I

I  A-B   I   63.3 I   42.2 I         I           I            I           I

I  A-C   I 1073.6 I  715.7 I         I           I            I           I

---------------------------------------------------------------------------

I  ALL   I 2188.5 I 1459.0 I    80.4 I    0.04   I      80.4  I    0.04   I

---------------------------------------------------------------------------

* DELAY IS THAT OCCURRING ONLY WITHIN THE TIME PERIOD

* INCLUSIVE DELAY INCLUDES DELAY SUFFERED BY VEHICLES

WHICH ARE STILL QUEUEING AFTER THE END OF THE TIME PERIOD

* THESE WILL ONLY BE SIGNIFICANTLY DIFFERENT IF THERE IS

A LARGE QUEUE REMAINING AT THE END OF THE TIME PERIOD.

*******END OF RUN*******

============================================= end of file ===============================================