TRL LIMITED

(C) COPYRIGHT 2006

CAPACITIES, QUEUES, AND DELAYS AT 3 OR 4-ARM MAJOR/MINOR PRIORITY JUNCTIONS

PICADY 5.1 ANALYSIS PROGRAM

RELEASE 4.0 (SEPT 2008)

ADAPTED FROM PICADY/3 WHICH IS CROWN COPYRIGHT

BY PERMISSION OF THE CONTROLLER OF HMSO

--------------------------------------------------------

FOR SALES AND DISTRIBUTION INFORMATION,

PROGRAM ADVICE AND MAINTENANCE CONTACT:

TRL SOFTWARE BUREAU

TEL: CROWTHORNE (01344) 770758, FAX: 770356

EMAIL: Software@trl.co.uk

--------------------------------------------------------

Run with file:-

"C:\Documents and Settings\Aiofe\Local Settings\temp\PICADY 5\PICADY5.vpi"

(drive-on-the-left) at 12:53:59 on Friday, 19 November 2010

.RUN INFORMATION

***************

RUN TITLE       : O' Devaney Gardens

LOCATION        : North Circular Road/O'Devaney Gardens

DATE            : 19/11/10

CLIENT          : Dublin City Council

ENUMERATOR      : Aoife [FUREY002]

JOB NUMBER      : 110/A59

STATUS          : TIA

DESCRIPTION     :

.MAJOR/MINOR JUNCTION CAPACITY AND DELAY

***************************************

INPUT DATA

----------

MAJOR ROAD (ARM C) --------------------- MAJOR ROAD (ARM A)

I

I

I

I

I

I

MINOR ROAD (ARM B)

ARM A IS North Circular Road East

ARM B IS O'Devaney Gardens

ARM C IS North Circular Road West

.STREAM LABELLING CONVENTION

---------------------------

STREAM  A-B  CONTAINS TRAFFIC GOING FROM ARM  A TO ARM B

STREAM  B-AC CONTAINS TRAFFIC GOING FROM ARM  B TO ARM A AND TO ARM  C

ETC.

.GEOMETRIC DATA

--------------

--------------------------------------------------------------------------------------

I                DATA ITEM                                       I   MINOR ROAD B    I

--------------------------------------------------------------------------------------

I  TOTAL MAJOR ROAD CARRIAGEWAY WIDTH                            I ( W  )  8.00 M.   I

I  CENTRAL RESERVE WIDTH                                         I (WCR )  0.00 M.   I

I                                                                I                   I

I  MAJOR ROAD RIGHT  TURN - WIDTH                                I (WC-B)  0.00 M.   I

I                         - VISIBILITY                           I (VC-B)120.00 M.   I

I                         - BLOCKS TRAFFIC                       I          YES      I

I                                                                I                   I

I  MINOR ROAD - VISIBILITY TO LEFT                               I (VB-C) 120.0 M.   I

I             - VISIBILITY TO RIGHT                              I (VB-A) 120.0 M.   I

I             - LANE 1 WIDTH                                     I (WB-C)  3.00 M.   I

I             - LANE 2 WIDTH                                     I (WB-A)  0.00 M.   I

--------------------------------------------------------------------------------------

.SLOPES AND INTERCEPT

--------------------

(NB:Streams may be combined, in which case capacity will be adjusted)

---------------------------------------------------------

I Intercept For Slope For Opposing   Slope For Opposing I

I STREAM B-C     STREAM  A-C          STREAM A-B        I

---------------------------------------------------------

I     769.51            0.27                0.11        I

---------------------------------------------------------

--------------------------------------------------------------------------------------------------

I Intercept For Slope For Opposing   Slope For Opposing   Slope For Opposing   Slope For OpposingI

I STREAM B-A     STREAM  A-C          STREAM A-B          STREAM  C-A          STREAM  C-B       I

--------------------------------------------------------------------------------------------------

I     635.97            0.27                0.11                  0.17                0.38       I

--------------------------------------------------------------------------------------------------

---------------------------------------------------------

I Intercept For Slope For Opposing   Slope For Opposing I

I STREAM C-B     STREAM  A-C          STREAM A-B        I

---------------------------------------------------------

I     643.46            0.23                0.23        I

---------------------------------------------------------

(NB These values do not allow for any site specific corrections)

.TRAFFIC DEMAND DATA

-------------------

-----------------------

I ARM I FLOW SCALE(%) I

-----------------------

I A   I      100      I

I B   I      100      I

I C   I      100      I

-----------------------

.Demand set:        O Devaney Gardens

TIME PERIOD BEGINS 07.45 AND ENDS  09.15

LENGTH OF TIME PERIOD  -   90 MIN.

LENGTH OF TIME SEGMENT -   15 MIN.

.DEMAND FLOW PROFILES ARE SYNTHESISED FROM TURNING COUNT DATA

------------------------------------------------------------------------------------

I        I   NUMBER OF MINUTES FROM START WHEN    I   RATE OF FLOW (VEH/MIN)       I

I  ARM   I FLOW STARTS I TOP OF PEAK I FLOW STOPS I BEFORE I AT TOP  I AFTER       I

I        I   TO RISE   I  IS REACHED I FALLING    I  PEAK  I OF PEAK I PEAK        I

I        I             I             I            I        I         I             I

------------------------------------------------------------------------------------

I ARM  A I     15.00   I     45.00   I    75.00   I 11.10  I  16.65  I 11.10       I

I ARM  B I     15.00   I     45.00   I    75.00   I  0.98  I   1.46  I  0.98       I

I ARM  C I     15.00   I     45.00   I    75.00   I 12.55  I  18.83  I 12.55       I

------------------------------------------------------------------------------------

.Demand set:        O Devaney Gardens

-----------------------------------------------------------

I                    I         TURNING PROPORTIONS        I

I                    I         TURNING COUNTS             I

I                    I        (PERCENTAGE OF H.V.S)       I

I                    --------------------------------------

I        TIME        I FROM/TO I ARM  A I ARM  B I ARM  C I

-----------------------------------------------------------

I   07.45 - 08.00    I         I        I        I        I

I                    I ARM  A  I  0.000 I  0.088 I  0.912 I

I                    I         I    0.0 I   78.0 I  810.0 I

I                    I         I (  0.0)I ( 10.0)I ( 10.0)I

I                    I         I        I        I        I

I                    I ARM  B  I  0.718 I  0.000 I  0.282 I

I                    I         I   56.0 I    0.0 I   22.0 I

I                    I         I ( 10.0)I (  0.0)I ( 10.0)I

I                    I         I        I        I        I

I                    I ARM  C  I  0.813 I  0.187 I  0.000 I

I                    I         I  816.0 I  188.0 I    0.0 I

I                    I         I ( 10.0)I ( 10.0)I (  0.0)I

I                    I         I        I        I        I

-----------------------------------------------------------

TURNING PROPORTIONS ARE CALCULATED FROM TURNING COUNT DATA

DEFAULT PROPORTIONS OF HEAVY VEHICLES ARE USED

.              QUEUE AND DELAY INFORMATION FOR EACH 15 MIN TIME SEGMENT

--------------------------------------------------------

FOR COMBINED DEMAND SETS

AND FOR TIME PERIOD        1

.------------------------------------------------------------------------------------------------------------------

I  TIME      DEMAND  CAPACITY  DEMAND/   PEDESTRIAN  START   END       DELAY     GEOMETRIC DELAY   AVERAGE DELAY I

I         (VEH/MIN) (VEH/MIN) CAPACITY      FLOW     QUEUE  QUEUE    (VEH.MIN/      (VEH.MIN/      PER ARRIVING  I

I                               (RFC)    (PEDS/MIN) (VEHS) (VEHS)  TIME SEGMENT)  TIME SEGMENT)    VEHICLE (MIN) I

I 07.45-08.00                                                                                                    I

I   B-AC      0.98      4.92    0.199                0.00   0.24        3.4                            0.25      I

I   C-A      10.24                                                                                               I

I   C-B       2.36      7.21    0.327                0.00   0.48        6.7                            0.20      I

I   A-B       0.98                                                                                               I

I   A-C      10.16                                                                                               I

I                                                                                                                I

.------------------------------------------------------------------------------------------------------------------

.------------------------------------------------------------------------------------------------------------------

I  TIME      DEMAND  CAPACITY  DEMAND/   PEDESTRIAN  START   END       DELAY     GEOMETRIC DELAY   AVERAGE DELAY I

I         (VEH/MIN) (VEH/MIN) CAPACITY      FLOW     QUEUE  QUEUE    (VEH.MIN/      (VEH.MIN/      PER ARRIVING  I

I                               (RFC)    (PEDS/MIN) (VEHS) (VEHS)  TIME SEGMENT)  TIME SEGMENT)    VEHICLE (MIN) I

I 08.00-08.15                                                                                                    I

I   B-AC      1.17      3.79    0.309                0.24   0.43        6.1                            0.38      I

I   C-A      12.23                                                                                               I

I   C-B       2.82      6.72    0.419                0.48   0.70       10.0                            0.25      I

I   A-B       1.17                                                                                               I

I   A-C      12.14                                                                                               I

I                                                                                                                I

.------------------------------------------------------------------------------------------------------------------

.------------------------------------------------------------------------------------------------------------------

I  TIME      DEMAND  CAPACITY  DEMAND/   PEDESTRIAN  START   END       DELAY     GEOMETRIC DELAY   AVERAGE DELAY I

I         (VEH/MIN) (VEH/MIN) CAPACITY      FLOW     QUEUE  QUEUE    (VEH.MIN/      (VEH.MIN/      PER ARRIVING  I

I                               (RFC)    (PEDS/MIN) (VEHS) (VEHS)  TIME SEGMENT)  TIME SEGMENT)    VEHICLE (MIN) I

I 08.15-08.30                                                                                                    I

I   B-AC      1.43      2.12    0.674                0.43   1.66       20.1                            1.19      I

I   C-A      14.97                                                                                               I

I   C-B       3.45      6.04    0.571                0.70   1.26       17.4                            0.38      I

I   A-B       1.43                                                                                               I

I   A-C      14.86                                                                                               I

I                                                                                                                I

.------------------------------------------------------------------------------------------------------------------

.------------------------------------------------------------------------------------------------------------------

I  TIME      DEMAND  CAPACITY  DEMAND/   PEDESTRIAN  START   END       DELAY     GEOMETRIC DELAY   AVERAGE DELAY I

I         (VEH/MIN) (VEH/MIN) CAPACITY      FLOW     QUEUE  QUEUE    (VEH.MIN/      (VEH.MIN/      PER ARRIVING  I

I                               (RFC)    (PEDS/MIN) (VEHS) (VEHS)  TIME SEGMENT)  TIME SEGMENT)    VEHICLE (MIN) I

I 08.30-08.45                                                                                                    I

I   B-AC      1.43      2.11    0.679                1.66   1.85       26.6                            1.40      I

I   C-A      14.97                                                                                               I

I   C-B       3.45      6.04    0.571                1.26   1.29       19.2                            0.38      I

I   A-B       1.43                                                                                               I

I   A-C      14.86                                                                                               I

I                                                                                                                I

.------------------------------------------------------------------------------------------------------------------

.------------------------------------------------------------------------------------------------------------------

I  TIME      DEMAND  CAPACITY  DEMAND/   PEDESTRIAN  START   END       DELAY     GEOMETRIC DELAY   AVERAGE DELAY I

I         (VEH/MIN) (VEH/MIN) CAPACITY      FLOW     QUEUE  QUEUE    (VEH.MIN/      (VEH.MIN/      PER ARRIVING  I

I                               (RFC)    (PEDS/MIN) (VEHS) (VEHS)  TIME SEGMENT)  TIME SEGMENT)    VEHICLE (MIN) I

I 08.45-09.00                                                                                                    I

I   B-AC      1.17      3.77    0.310                1.85   0.47        8.2                            0.41      I

I   C-A      12.23                                                                                               I

I   C-B       2.82      6.72    0.419                1.29   0.74       11.8                            0.26      I

I   A-B       1.17                                                                                               I

I   A-C      12.14                                                                                               I

I                                                                                                                I

.------------------------------------------------------------------------------------------------------------------

.------------------------------------------------------------------------------------------------------------------

I  TIME      DEMAND  CAPACITY  DEMAND/   PEDESTRIAN  START   END       DELAY     GEOMETRIC DELAY   AVERAGE DELAY I

I         (VEH/MIN) (VEH/MIN) CAPACITY      FLOW     QUEUE  QUEUE    (VEH.MIN/      (VEH.MIN/      PER ARRIVING  I

I                               (RFC)    (PEDS/MIN) (VEHS) (VEHS)  TIME SEGMENT)  TIME SEGMENT)    VEHICLE (MIN) I

I 09.00-09.15                                                                                                    I

I   B-AC      0.98      4.90    0.200                0.47   0.25        4.0                            0.26      I

I   C-A      10.24                                                                                               I

I   C-B       2.36      7.21    0.327                0.74   0.50        7.8                            0.21      I

I   A-B       0.98                                                                                               I

I   A-C      10.16                                                                                               I

I                                                                                                                I

.------------------------------------------------------------------------------------------------------------------

.

QUEUE FOR STREAM    B-AC

-------------------------

TIME          NO. OF

SEGMENT       VEHICLES

ENDING        IN QUEUE

08.00           0.2

08.15           0.4

08.30           1.7    **

08.45           1.9    **

09.00           0.5

09.15           0.3

.

QUEUE FOR STREAM    C-B

-------------------------

TIME          NO. OF

SEGMENT       VEHICLES

ENDING        IN QUEUE

08.00           0.5

08.15           0.7    *

08.30           1.3    *

08.45           1.3    *

09.00           0.7    *

09.15           0.5

.

QUEUEING DELAY INFORMATION OVER WHOLE PERIOD

--------------------------------------------

---------------------------------------------------------------------------

I STREAM I   TOTAL DEMAND  I   * QUEUEING *      I * INCLUSIVE QUEUEING * I

I        I                 I    * DELAY *        I       * DELAY *        I

I        I----------------------------------------------------------------I

I        I  (VEH)  (VEH/H) I  (MIN)    (MIN/VEH) I    (MIN)     (MIN/VEH) I

---------------------------------------------------------------------------

I  B-AC  I  107.4 I   71.6 I    68.5 I    0.64   I      68.5  I    0.64   I

I  C-A   I 1123.2 I  748.8 I         I           I            I           I

I  C-B   I  258.8 I  172.5 I    73.0 I    0.28   I      73.0  I    0.28   I

I  A-B   I  107.4 I   71.6 I         I           I            I           I

I  A-C   I 1114.9 I  743.3 I         I           I            I           I

---------------------------------------------------------------------------

I  ALL   I 2711.6 I 1807.7 I   141.5 I    0.05   I     141.5  I    0.05   I

---------------------------------------------------------------------------

* DELAY IS THAT OCCURRING ONLY WITHIN THE TIME PERIOD

* INCLUSIVE DELAY INCLUDES DELAY SUFFERED BY VEHICLES

WHICH ARE STILL QUEUEING AFTER THE END OF THE TIME PERIOD

* THESE WILL ONLY BE SIGNIFICANTLY DIFFERENT IF THERE IS

A LARGE QUEUE REMAINING AT THE END OF THE TIME PERIOD.

*******END OF RUN*******

============================================= end of file ===============================================